Rodrigo Becerril Ferreyra
Dr. Gevik Sardarbegian
CECS 440 Section 02
26 October 2021
Lab 4
This lab tasked us with creating a 16-bit Arithmetic Logic Unit (ALU) from 16 different 1-bit ALUs that can add, subtract, OR, or AND two bits. Both ALU modules were verified with the code I provided below. The full adder module was verified last lab. I did not verify the multiplexer, AND gate, or OR gate modules because they are very simple. To verify these, I simply looked at the block diagram that was created using the Elaborated Design feature of Vivado. Note that I performed modifications on the multiplexer module, because the block diagram looked very off, and I could not guarantee that it works as intended. Additionally, your version uses RTL_LATCHES. These latches should be avoided at all costs, unless the designer explicitly creates one. Latches mean that there is likely a case statement that does not consider all options. Here are the block diagram for your mux module and mine:

Please note that high-quality vector .pdf files of these images are available in the Lab submission. The following source files are also available there.
full_adder.vhd

--------------------------------------------------------------------------------
-- Company: California State University, Long Beach
-- Engineer: Rodrigo Becerril Ferreyra
--
-- Create Date: 10/12/2021 11:54:07 PM
-- Design Name: full_adder
-- Module Name: full_adder
-- Project Name: CECS 440 Lab 3
-- Description: A simple 1-bit wide full adder.
--
-- Dependencies:
--
-- Revision: 1
--------------------------------------------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.NUMERIC_STD.ALL;
entity full_adder is
   port
   (
       a: in std_logic;
       b: in std_logic;
       cin: in std_logic;
       sum: out std_logic;
       cout: out std_logic
   );
end full_adder;
architecture Behavioral of full_adder is
begin
   -- two simple assign statements for a one-bit adder
   sum <= a xor b xor cin;
   cout <= (a and b) or (b and cin) or (cin and a);
end Behavioral;

and_gate.vhd

Library ieee;
Use ieee.std_logic_1164.all;
Use ieee.std_logic_unsigned.all;
Entity and_gate is
port(
In1	:	in	std_logic;
In2	:	in	std_logic;
Sout	:	out	std_logic
);
End;
Architecture behavior of and_gate is
Begin
-- In1 In2 Sout
-- 0 0 0
-- 0 1 0
-- 1 0 0
-- 1 1 1
-- and gate logic
Sout <= In1 and In2;
End;

or_gate.vhd

----------------------------------------------------------------------------------
-- Company: California State University, Long Beach
-- Engineer: Rodrigo Becerril Ferreyra
--
-- Create Date: 10/25/2021 11:46:06 AM
-- Module Name: or_gate - Behavioral
-- Project Name: Lab 4
----------------------------------------------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
--use IEEE.NUMERIC_STD.ALL;
entity or_gate is
   port
   (
       In1 : in std_logic;
       In2 : in std_logic;
       Sout: out std_logic
   );
end or_gate;
architecture Behavioral of or_gate is
begin
   Sout <= In1 or In2;
end Behavioral;

MUX31.vhd

----------------------------------------------------------------------------------
-- Company: California State University, Long Beach
-- Engineer: Rodrigo Becerril Ferreyra
-- Module Name: MUX31 - Behavioral
-- Project Name: Lab 4
-- Description: I improved the mux block (is now an actual mux).
-- The last version had an RTL_LATCH in it, which I hear is something to avoid
----------------------------------------------------------------------------------
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
entity MUX31 is
   -- define ports
   port
   (
       Input1: in std_logic;
       Input2: in std_logic;
       Input3: in std_logic;
       S: in std_logic_vector(1 downto 0);
       Sout: out std_logic
   );
end MUX31;
architecture Behavioral of MUX31 is
begin
   process (S, Input1, Input2, Input3)
   begin
       case S is
        when "00" => Sout <= Input1;
        when "01" => Sout <= Input1;
        when "10" => Sout <= Input2;
        when "11" => Sout <= Input3;
        when others => Sout <= 'Z';
       end case;
   end process;
end Behavioral;

ALU1bit.vhd

----------------------------------------------------------------------------------
-- Company: California State University, Long Beach
-- Engineer: Rodrigo Becerril Ferreyra
--
-- Create Date: 10/25/2021 11:31:08 AM
-- Module Name: ALU1bit - Behavioral
-- Project Name: Lab 4
----------------------------------------------------------------------------------
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
use IEEE.NUMERIC_STD.ALL;
-- assign top-level ports
entity ALU1bit is
   port(
        A : in std_logic;
        B : in std_logic;
        Cin : in std_logic;
        S : in std_logic_vector(1 downto 0);
        Sout : out std_logic;
        Cout : out std_logic
   );
end ALU1bit;
Architecture behavior of ALU1bit is
   -- intstantiate full_adder module
   component full_adder
       port
       (
        a : in std_logic;
        b : in std_logic;
        cin : in std_logic;
        sum : out std_logic;
        cout : out std_logic
       );
   end component;
   -- intstantiate MUX31 module
   component MUX31
       port
       (
        Input1 : in std_logic;
        Input2 : in std_logic;
        Input3 : in std_logic;
        S : in std_logic_vector(1 downto 0);
        Sout : out std_logic
       );
   end component;
   -- intstantiate and_gate module
   component and_gate
       port
       (
        In1 : in std_logic;
        In2 : in std_logic;
        Sout : out std_logic
       );
   end component;
   -- intstantiate or_gate module
   component or_gate
   port
   (
       In1 : in std_logic;
       In2 : in std_logic;
       Sout : out std_logic
   );
   end component;
   -- signal definitions
   signal Sout_full_adder: std_logic;
   signal Sout_and_gate : std_logic;
   signal Sout_or_gate : std_logic;
   signal Xor_out : std_logic;
   signal Cin_muxed : std_logic;
begin
   -- assign statements
   -- flips B if S(0) is 1
   Xor_out <= B xor S(0);
   -- If S(0) is set (subtract mode), then a 1 should always go into the
   -- Cin port on the full adder (two's compliment is flip all bits
   -- then add 1). If S(0) is cleared, then simply pass Cin into
   -- the Cin port in full_adder.
   --with S(0) select Cin_muxed <= '1' when '1', Cin when '0', 'Z' when others;
   fulladderblock: full_adder
   port map
   (
       a => A,
       b => Xor_out,
       cin => Cin,
       sum => Sout_full_adder,
       cout => Cout
   );
   andgateblock: and_gate
   port map
   (
       In1 => A,
       In2 => B,
       Sout => Sout_and_gate
   );
   orgateblock: or_gate
   port map
   (
       In1 => A,
       In2 => B,
       Sout => Sout_or_gate
   );
   muxblock: MUX31
   port map
   (
       Input1 => Sout_full_adder,
       Input2 => Sout_and_gate,
       Input3 => Sout_or_gate,
       S => S,
       Sout => Sout
   );
end;
ALU16bit.vhd

----------------------------------------------------------------------------------
-- Company: California State University, Long Beach
-- Engineer: Rodrigo Becerril Ferreyra
--
-- Create Date: 10/25/2021 01:23:54 PM
-- Module Name: ALU16bit - Behavioral
-- Project Name: Lab 4
----------------------------------------------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
--use IEEE.NUMERIC_STD.ALL;
-- define top-level ports for ALU16bit
entity ALU16bit is
   port
   (
       A: in std_logic_vector(15 downto 0);
       B: in std_logic_vector(15 downto 0);
       S: in std_logic_vector(1 downto 0);
       Cout: out std_logic;
       Sout: out std_logic_vector(15 downto 0)
   );
end ALU16bit;
architecture Behavioral of ALU16bit is
   -- ALU1bit declaration
   component ALU1bit
       port(
        A : in std_logic;
        B : in std_logic;
        Cin : in std_logic;
        S : in std_logic_vector(1 downto 0);
        Sout : out std_logic;
        Cout : out std_logic
       );
   end component;
   -- cin-cout inbetween wires
   signal inbetween: std_logic_vector(14 downto 0);
begin
   Sum0: ALU1bit
   port map
   (
       A => A(0),
       B => B(0),
       Cin => S(0),
       S => S,
       Cout => inbetween(0),
       Sout => Sout(0)
   );
   Sum1: ALU1bit
   port map
   (
       A => A(1),
       B => B(1),
       Cin => inbetween(0),
       S => S,
       Cout => inbetween(1),
       Sout => Sout(1)
   );
   Sum2: ALU1bit
   port map
   (
       A => A(2),
       B => B(2),
       Cin => inbetween(1),
       S => S,
       Cout => inbetween(2),
       Sout => Sout(2)
   );
   Sum3: ALU1bit
   port map
   (
       A => A(3),
       B => B(3),
       Cin => inbetween(2),
       S => S,
       Cout => inbetween(3),
       Sout => Sout(3)
   );
   Sum4: ALU1bit
   port map
   (
       A => A(4),
       B => B(4),
       Cin => inbetween(3),
       S => S,
       Cout => inbetween(4),
       Sout => Sout(4)
   );
   Sum5: ALU1bit
   port map
   (
       A => A(5),
       B => B(5),
       Cin => inbetween(4),
       S => S,
       Cout => inbetween(5),
       Sout => Sout(5)
   );
   Sum6: ALU1bit
   port map
   (
       A => A(6),
       B => B(6),
       Cin => inbetween(5),
       S => S,
       Cout => inbetween(6),
       Sout => Sout(6)
   );
   Sum7: ALU1bit
   port map
   (
       A => A(7),
       B => B(7),
       Cin => inbetween(6),
       S => S,
       Cout => inbetween(7),
       Sout => Sout(7)
   );
   Sum8: ALU1bit
   port map
   (
       A => A(8),
       B => B(8),
       Cin => inbetween(7),
       S => S,
       Cout => inbetween(8),
       Sout => Sout(8)
   );
   Sum9: ALU1bit
   port map
   (
       A => A(9),
       B => B(9),
       Cin => inbetween(8),
       S => S,
       Cout => inbetween(9),
       Sout => Sout(9)
   );
   Sum10: ALU1bit
   port map
   (
       A => A(10),
       B => B(10),
       Cin => inbetween(9),
       S => S,
       Cout => inbetween(10),
       Sout => Sout(10)
   );
   Sum11: ALU1bit
   port map
   (
       A => A(11),
       B => B(11),
       Cin => inbetween(10),
       S => S,
       Cout => inbetween(11),
       Sout => Sout(11)
   );
   Sum12: ALU1bit
   port map
   (
       A => A(12),
       B => B(12),
       Cin => inbetween(11),
       S => S,
       Cout => inbetween(12),
       Sout => Sout(12)
   );
   Sum13: ALU1bit
   port map
   (
       A => A(13),
       B => B(13),
       Cin => inbetween(12),
       S => S,
       Cout => inbetween(13),
       Sout => Sout(13)
   );
   Sum14: ALU1bit
   port map
   (
       A => A(14),
       B => B(14),
       Cin => inbetween(13),
       S => S,
       Cout => inbetween(14),
       Sout => Sout(14)
   );
   Sum15: ALU1bit
   port map
   (
       A => A(15),
       B => B(15),
       Cin => inbetween(14),
       S => S,
       Cout => Cout,
       Sout => Sout(15)
   );
end Behavioral;
ALU1bit_tb.vhd

----------------------------------------------------------------------------------
-- Company: California State University, Long Beach
-- Engineer: Rodrigo Becerril Ferreyra
--
-- Create Date: 10/25/2021 12:37:32 PM
-- Module Name: ALU1bit_tb - Behavioral
-- Project Name: Lab 4
----------------------------------------------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
--use IEEE.NUMERIC_STD.ALL;
entity ALU1bit_tb is
end ALU1bit_tb;
architecture Behavioral of ALU1bit_tb is
   -- declare unit under test
   component ALU1bit
       port
       (
        A : in std_logic;
        B : in std_logic;
        Cin : in std_logic;
        S : in std_logic_vector(1 downto 0);
        Sout : out std_logic;
        Cout : out std_logic
       );
   end component;
   -- declare signals
   signal A_tb: std_logic := '0';
   signal B_tb: std_logic := '0';
   signal Cin_tb: std_logic := '0';
   signal S_tb: std_logic_vector(1 downto 0) := "00";
   signal Sout_tb: std_logic;
   signal Cout_tb: std_logic;
   constant tick: time := 100 ns;
begin
   -- instantiate ALU1bit as uut
   uut: ALU1bit
   port map
   (
       A => A_tb,
       B => B_tb,
       Cin => Cin_tb,
       S => S_tb,
       Sout => Sout_tb,
       Cout => Cout_tb
   );
   -- process to change A
   process
   begin
       wait for tick;
       A_tb <= not A_tb;
   end process;
   -- process to change B
   process
   begin
       wait for (tick*2);
       B_tb <= not B_tb;
   end process;
   -- process to change Cin
   process
   begin
       wait for (tick*4);
       Cin_tb <= not Cin_tb;
   end process;
   -- process to change S(0)
   process
   begin
       wait for (tick*8);
       S_tb(0) <= not S_tb(0);
   end process;
   -- process to change S(1)
   process
   begin
       wait for (tick*16);
       S_tb(1) <= not S_tb(1);
   end process;
end Behavioral;

ALU16bit_tb.vhd

----------------------------------------------------------------------------------
-- Company: California State University, Long Beach
-- Engineer: Rodrigo Becerril Ferreyra
--
-- Create Date: 10/25/2021 04:45:35 PM
-- Module Name: ALU16bit_tb - Behavioral
-- Project Name: Lab 4
----------------------------------------------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
--use IEEE.NUMERIC_STD.ALL;
entity ALU16bit_tb is
end ALU16bit_tb;
architecture Behavioral of ALU16bit_tb is
   -- define unit to test
   component ALU16bit
       port
       (
        A: in std_logic_vector(15 downto 0);
        B: in std_logic_vector(15 downto 0);
        S: in std_logic_vector(1 downto 0);
        Cout: out std_logic;
        Sout: out std_logic_vector(15 downto 0)
       );
   end component;
   -- define signals
   signal A_tb: std_logic_vector(15 downto 0) := "0000000000000000";
   signal B_tb: std_logic_vector(15 downto 0) := "0000000000000000";
   signal S_tb: std_logic_vector(1 downto 0) := "00";
   signal Cout_tb: std_logic;
   signal Sout_tb: std_logic_vector(15 downto 0);
   constant tick: time := 50 ns;
begin
   -- instantiate ALU16bit and tie inputs/outputs
   uut: ALU16bit
   port map
   (
       A => A_tb,
       B => B_tb,
       S => S_tb,
       Cout => Cout_tb,
       Sout => Sout_tb
   );
   -- main process
   process
   begin
       S_tb <= "00";
       A_tb <= x"0096"; -- 150
       B_tb <= x"0104"; -- 260
       wait for tick;
       S_tb <= "00";
       A_tb <= x"FFE7"; -- -25
       B_tb <= x"0041"; -- 65
       wait for tick;
       S_tb <= "00";
       A_tb <= x"0002"; -- 2
       B_tb <= x"0002"; -- 2
       wait for tick;
       S_tb <= "01";
       A_tb <= x"0226"; -- 550
       B_tb <= x"0140"; -- 320
       wait for tick;
       S_tb <= "01";
       A_tb <= x"0019"; -- 25
       B_tb <= x"003C"; -- 60
       wait for tick;
       S_tb <= "01";
       A_tb <= x"FFFE"; -- -2
       B_tb <= x"0010"; -- 16
       wait for tick;
       S_tb <= "10";
       A_tb <= x"0040"; -- 64
       B_tb <= x"0100"; -- 256
       wait for tick;
       S_tb <= "10";
       A_tb <= x"07D0"; -- 2000
       B_tb <= x"0003"; -- 3
       wait for tick;
       S_tb <= "10";
       A_tb <= x"14DE"; -- 5342
       B_tb <= x"03DA"; -- 986
       wait for tick;
       S_tb <= "11";
       A_tb <= x"000C"; -- 12
       B_tb <= x"0007"; -- 7
       wait for tick;
       S_tb <= "11";
       A_tb <= x"0000"; -- 0
       B_tb <= x"0929"; -- 2345
       wait for tick;
       S_tb <= "11";
       A_tb <= x"FFFF"; -- -1
       B_tb <= x"0005"; -- 5
       wait for tick;
       -- exits the simulation
       report "simulation finished successfully" severity FAILURE;
   end process;
end Behavioral;

Results:
S1	S0	A	B	Sout	Cout
0	0	150	260	410	0
0	0	-25	65	40	1
0	0	2	2	4	0
0	1	550	320	230	1
0	1	25	60	-35	0
0	1	-2	16	-18	1
1	0	64	256	0	0
1	0	2000	3	0	0
1	0	5342	968	218	0
1	1	12	7	15	1
1	1	0	2345	2345	0
1	1	-1	5	-1	1